## Slide 1
SATA
Pouria
Ghafouri

## Slide 2
Table of Contents
Introduction
Overview of SATA, its role in storage connectivity
01
Evolution & Overview of SATA
History, Versions (SATA I, II, II)
02
SATA Architecture
Layered model: Physical, Link, Transport, Application
03
Physical Layer
Signaling, connector/cable design
04
Transport Layer – FIS Structures
FIS types, NCQ
06
Message flow and command
SATA controllers
07
Summary
08
Link Layer
Encoding, Flow Control, Error Detection
05

## Slide 3
Introduction
What is SATA?
  Stands for Serial Advanced Technology Attachment
  A Serial Interface Standard
  Connects Storage to a computer’s motherboard
  Replaces the older parallel ATA (PATA)

## Slide 4
Introduction
Key Features
  Serial Communication: Better than PATA
  Hot-Plugging
  No Timing Skew
  Point-to-Point Technology

## Slide 5
Pre-SATA Era
  Parallel ATA (PATA) dominate storage interfaces until the early 2000s
  Limitations of PATA (More wires, Slower Speed max 133 MB/s)
SATA Introduction
  Developed by the SATA-IO consortium (Serial ATA International Organization) in 2000
  Replace PATA with a faster, simpler and more scalable interface
  First released in 2003 as SATA 1.0

## Slide 6
SATA 3.0 2009
Improved NCQ for deeper queues
6 Gb/s
Enhanced power management
SATA 2.0 2004
Mandatory NCQ
3 Gb/s
Hot-plugging support
SATA 1.0 2003
First-generation serial Interface
1.5 Gb/s
Add Optional NCQ (Native Command Queuing)

## Slide 7
Physical Layer
Link Layer
Transport Layer
Application Layer
Electrical and physical connection between the SATA controller and the drive
Differential signaling with TX and RX
Point-to-Point topology
Utilize OOB (Out-of-Band) signaling
Uses 8b/10b encoding
Controls flow control
Error Detection using CRC
Handles Link Power Management (LPM) to reduce power consumption
Organizes data into frames called FIS (Frame Information Structure)
Implements commands such as DMA
Features like NCQ
Implements ATA command sets (read, write, flush, ...)
Supports features like TRIM (for SSDs)
SMART (self-Monitoring, Analysis and Reporting Technology)

## Slide 10
FIS
FIS
FIS (Frame Information Structure)
  FIS is the fundamental data packet used by SATA to communicate between the host and storage device
  Structure:
    Header: Specifies FIS type, direction, and control flags. (1 Byte)
    Payload: Contains command parameters, sector addresses or actual data. (4 to 32 bytes)
    CRC: 32-bit checksum for error detection

## Slide 11
FIS
FIS
Transmit ATA commands (READ, WRITE) and parameters to the device
Register FIS H2D
DMA Activate FIS
Initiates DMA transfers by specifting memory addresses for data exchange
Register FIS D2H
Returns status updates (command completion, errors)
Data FIS
Carries payload data during read/write operations

## Slide 12
FIS
FIS
NCQ (Native Command Queuing)
  Optimize commands to minimize delays (Mechanical delays HDDs, Latency SSDs)
  Supported in SATA II and later (in SATA I was optional)

## Slide 13
FIS
FIS