## Slide 1: 10BASE-T Ethernet
Amir Hasan Jafarabadi

## Slide 2: What is Ethernet
Connects computers and other devices within a local area network (LAN).
Layer 1 & 2 network protocol
First developed at Xerox PARC in the 1970s, , later standardized by IEEE as 802.3 family
Supports speeds ranging from 2 Mbps in older versions to 400 Gbps

## Slide 3: Ethernet History
1973: First Ethernet prototype (2.94 Mbps, coaxial cable).
1980: Digital, Intel, and Xerox (DIX) publish the first Ethernet specification.
1983: IEEE 802.3 standard officially released (10 Mbps over coaxial).
1990: Introduction of 10BASE-T (twisted pair, star topology).
1995: Fast Ethernet (100BASE-T) introduced.
1999: Gigabit Ethernet (1000BASE-T) standardized.
2010s: 10GbE, 40GbE, and beyond.

## Slide 4: 10BASE-T
Definition: 10 Megabit Ethernet over twisted pair cables
IEEE Standard: 802.3i (1990).
Physical Medium: Uses Cat3 or higher UTP cables with 8P8C connectors (100m maximum).
Signal:+2.5v and -2.5v voltage.
Network Topology: Star topology with a central hub or switch.
Innovation: Shifted Ethernet from coaxial bus to twisted pair wiring, making networks more reliable and scalable.

## Slide 5: Naming Convention
10, 100, 1000, 10G, ... – nominal, usable speed at the top of the physical layer
BASE, BROAD, PASS – indicates baseband, broadband, or passband
-T, -T1, -F, -S, -L - medium: T = twisted pair, -T1 = single-pair twisted pair, …
X, R – encoding method (varying with the generation): X for 4b/5b or 8b/10b, R for 64b/66b

## Slide 6: Twisted Pair
Structure: Twisted pair cables consist of pairs of copper wires twisted together to reduce electromagnetic interference.
Evolution: Initially used Category 3 cables; later, Cat5 and higher became common
Function: Uses two twisted pairs—one for transmitting and one for receiving data.

## Slide 7: RJ45 Connector
Standard 8P8C (8 Position, 8 Contact) connector.
Supports full-duplex and half-duplex operation.

## Slide 8: Crossover vs. Straight-Through Cables
Straight-Through Cable: Used to connect different types of devices (e.g., PC to switch, switch to router).
Crossover Cable: Used for direct device-to-device connections (e.g., PC to PC, switch to switch).
Pin Configuration: Straight-through cables have identical pinouts on both ends, while crossover cables swap Tx and Rx pairs.
Modern Usage: Auto MDI-X in modern switches makes crossover cables less necessary.

## Slide 9: MAC Address
A unique identifier assigned to a network interface controller (NIC)
48-bit (6-byte) identifiers usually represented in hexadecimal notation (e.g., 00:1A:2B:3C:4D:5E).
They are globally unique and assigned by device manufacturers,
used in Ethernet, Wi-Fi, and Bluetooth.
The Address Resolution Protocol (ARP) maps IP addresses to MAC addresses.

## Slide 10: Hubs vs Switches
Early Ethernet used hubs, which broadcast traffic to all connected devices.
Hubs operate at Layer 1 (physical layer) and do not process MAC addresses.
Collisions were common, making CSMA/CD necessary for network stability.
Switches (Layer 2) route frames intelligently, reducing collisions and improving efficiency.
Transition to switches happened as costs dropped and network demands increased.

## Slide 11: Collision Detection (CSMA/CD)
Carrier Sense: Devices listen before transmitting to avoid collisions.
Multiple Access: Multiple devices share the same medium.
Collision Detection: Detects overlapping transmissions and stops sending.
Jam Signal: signal sent to show collision
Backoff Algorithm: Devices wait a exponential random time before retrying.
Limitation: Becomes inefficient in high-traffic networks.

## Slide 12: Signal Encoding
Manchester Encoding: Ensures clock synchronization and signal integrity.
Voltage Levels: Uses two voltage levels for encoding data.
Synchronization: Every bit contains a transition for error detection.
Error Detection: Detects line interference and transmission issues.
Legacy: Used before more efficient encoding methods.

## Slide 13: Ethernet Packet
Preamble (7 byte alternating 0s and 1s)
Start of frame delimiter (1 byte: 10101011)
Destination MAC
Source MAC
4-byte optional tag
2-byte length
Payload
4-byte CRC

## Slide 14: Sources
https://www.practicalnetworking.net/stand-alone/ethernet-wiring/
https://arstechnica.com/gadgets/2011/07/ethernet-how-does-it-work/#page-3

## Slide 15: Thank You